## Slide 1: HW&SW Codesign Academy Case Study - ACME
Team 2
Martina Corda, Tomaz Maia Suller, Mattia Sironi

## Slide 2: Agenda
Goal 1
  Topology and Message Definition
  Implementation
  Challenges Faced during Implementation
  Conclusions and Lesson Learned
Goal 2
  Recap on the Requirements
  Syntethic Data Generation
  Challenges with GenAI
  Forecast Analysis
  Threshold Estimation

## Slide 3: Goal 1: Distributed Line Control

## Slide 4: Topology and Message Definition
Shared format for reading messages
  No need to define extra format for status
  Bigger message with "dummy" fields for Alert and Fault
Control messages
  Broker sends temperature threshold to gateway, which forwards to line controllers
  Gateway forwards sampling frequency to contorllers

## Slide 5: Implementation
On Arduino Nano RP2040:
  Temperature measurement
  Inner state switch logic
  Serial message preparation (UART)
On Arduino MKR WIFI 1010:
  Received message parser
  State switch for other lines logic
  MQTT server connection

## Slide 6: Challenges Faced during Implementation (1)
Understanding capabilities of provided HW
  Arduino documentation not explicit on how serial communication lines are distributed
  Number of UART controllers constrains design
  SoftwareSerial not supported by Arduino Nano RP2040

## Slide 7: Challenges Faced during Implementation (2)
Debugging external issues
  Connection to MQTT server successful initially
  No connection possible since Saturday
  Conclusion: MQTT server down (?)

## Slide 8: Conclusions and Lessons Learned
Results
Code implementation not complete
Working communication that involves both boards
Lesson Learned
Even a sample use case in embedded systems could cause big problems

## Slide 9: Demo Time!

## Slide 10: Goal 2: Adaptive Thresholding using ML

## Slide 11: Recap on the Requirement
Identify and develop an adaptive solution to monitor plant historical data, to forecast the optimal temperature thresholds according to site location and to adapt the plant configuration.
Synthetic Data creation:
  The data should cover a realistic sample of data (at least one each 10 minutes) simulating realistic temperature range within the 24h day and within the day of the year
  Part of the data (e.g. sample from the last year) should be used to test the forecasting capabilities of the chosen algorithm.
Timeseries Forecasting

## Slide 12: Synthetic Data Generation (1)
We asked chatGPT to create a code for generating synthetic data
Sinusoidal behaviour + random noise

## Slide 13: Synthetic Data Generation (2)
We didn’t like the sinusoidal behaviour across the years so we changed the code and we obtained the following pattern

## Slide 14: Challenges with GenAI
Unstability problems in the code generated via ChatGPT
Modification of the model order parameters

## Slide 15: Time Series Forecasting
Timeseries forecasting
The dataset generated was split into
  training set = 80% of dataset
  test set = 20% of the dataset
SARIMA model estimation using the training set
The test set was further divided into two dataset
  test set = 99.9% of the test set
  validation set = 0.01% of the test test ( to assess the quality of the forecasting)

## Slide 16: Forecast Analysis
The first days are well predicted but the drift is present as the number of days increase

## Slide 17: Threshold Estimation
Fixed approach based on estimated average daily temperature
Given lack of data from plant, no specific algorithm was designed

## Slide 18: Thank you!
Questions?